# Pos.	Quantity	Unit	Article/work			Unit price EUR	 	Total EUR

transfer:		_______,____

2.				Plastifloor-coating

2.01			m²	Prime prepared surface until all

pores are sealed.

Material:		Plastifloor 112

Material consump:	0.5 kg/m² per layer until

all pores are sealed

Broadcast with quartz sand 0.2-0.7 mm.

_______,____		_______,____

OPTION

2.02			kg/h	Levelling works

Deep or large holes and cavities,

eruptions or extreme flaws in the

substrate are eliminated in advance

on site or on customer’s directive

by our staff on direct labour, with

wage and material cost statement.

Technician work hour:

Resin-based mortar: Plastifloor® 510

An even floor coating, corresponding

to  DIN 18202, can only be achieved if

a correspondingly even substrate

exists or is established on customer’s

directive.			_______,____		_______,____

OPTION

2.03			kg/h	If there is no sufficient slope on site

(~ 2 %), this can be installed with reactive

resin-based mortar on customer’s directive

by our staff on direct labour, with

wage and material cost statement.

. 				If the coating is installed without

____________

Continued on page 3						transfer:		_______,_____

# Pos.	Quantity	Unit	Article/work			Unit price EUR	 	Total EUR

transfer:		    _______,____

sufficient slope, puddles on the floor

cannot be excluded.

1 kg resin-based mortar: Plastifloor® 510

1 h processing time	:	_______,____		_______,____

2.04			m	Force-fitly cast elaborated construction

joints and cracks.

Joint dimension:

Material: 	Plastifloor 510

Consumption:	   kg/m		_______,____		_______,____

2.04a			m	Form elaborated expansion joints

in the structure permanently elastic.

or install a suitable metal joint profile.

Joint dimension:

Material.	Plastifloor 430

Consumption:	   kg/m		________,____	________,____

2.05			m²	Coat the Plastifloor-broadcast coating

a toothed squeegee and draw off,

de-aerate with spike roller if required

layer thickness:	3-4 mm

Material consump:	2.5 kg resin mixture,

Plastifloor 332/V

1.25 kg quartz sand 0.06 – 0.2 mm

Broadcast the coating’s entire surface when

still wet with colour quartz sand 0.7 – 1.2 mm

S 1 – S 12 or 417

Material consump:	~ 5-6 kg/m²

_______,____		_______,______

Slip resistance R 11- R 12

Colour on customer’s request. Due to the

manufacturer, colour and mixture deviations

are possible. They do not lead to warranty

claims.

Manufacturer:	Plasti-Chemie International GmbH

Zum Plom 35

08541 Neuensalz

------------------------

____________

Continued on page 4						transfer:		________,___

# Pos.	Quantity	Unit	Article/work			Unit price EUR	 	Total EUR

transfer:		    _______,____

phone: 03741/5583-0

fax: 03741/5583-27

2.06			m²	Seal the coated surface.

Sealing must be effected until all

pores are sealed.

Material:		Plastifloor 528

Material consump:	0.6 kg/m²

3.				Site equipment

3.01			all in	- Setting up the site, provide tools

Machines during the whole con-

struction period.

- Executing and recording CM-measuring

- Executing and recording 1 bond strength

measurement

- Dispose of empty bundles environmentally

friendly

- Approach and departure from site 1 x

- Expense allowance for our staff

_______,____ 	_______,____

TITLE SUMMARY

1. Floor preparation

2. Plastifloor-coating

3. Site equipment

____________

Net amount						_______,____

VAT					_____ %	_______,____

--------------------

Total amount						_______,_____