REQUEST			Bill of quantities for

Plastifloor®-coating on metallic substrate

(e g.: steel sheet also hot-dip galvanised)

# Pos.	Quantity	Unit	Article/work			Unit price EUR	 	Total EUR

1.00			m²	Application of coating mass with a

Layer thickness of 1-2mm minimum,

Full-surface broadcasting with quartz sand

size 0.7-1.2mm

Sweeping off/vacuuming of excess quartz

sand after the coating has cured

Material:	Plastifloor 418/25 binder

with addition of adhesive agent HP 0.2 %

and Plastifloor hardener powder as per dosage chart

Material consump:	~ 1.5- kg/m² PF 418

~ 3-4 kg/m² quartz sand

m²					_______,____		_______,____

2.00			m²	Seal the coated surface.

Material:		Plastifloor 528

Material consump:	0.5-0.7 kg/m²

Colour: acc. RAL colour chart______,____		_______,____

Site equipment

4.00			all in	- Setting up the site, provide tools

Machines during the whole con-

struction period

Dispose of empty bundles environmentally

friendly

- Approach and departure from site 1 x

- Expense allowance for our staff										_______,____		_______,____

TITLE SUMMARY

Substrate preparation

Plastifloor®-coating

Plastifloor®-sealing

Site equipment

____________

Net amount						_______,_____

VAT			____ %			_______,_____

Total amount						_______,_____